## Slide 1: Le Grande Tour of FPGA Land
Jim Brakefield

## Slide 2: Introduction
LEGO Land:
  4M LUTs running at 500MHz = ~2*1015 ops/sec
uP Star-Trek slogan:
  Take microprocessors (uP) where no uP has gone before
FPGA Dr. Who slogan:
  FPGAs are for Time Lords: you have both time & space at your disposal

## Slide 3: FPGA (Field Programmable Gate Array) Table of Contents
FPGA 101
FPGA vendors
FPGA tools
  Sample project
IP & 3rd party designs
FPGA 201
Monster FPGAs
Neat projects
Literature & Videos
Design guidelines
Personal insights
Vendor histories
References

## Slide 4: FPGA 101
LUT Lookup table, 3..6 inputs, 1..2 out
DFF D flip-flop, 1 or 2 per LUT
IO Tristate transceiver, optional DFFs
Block RAM Dual port, .5K to 300K bits, variable aspect ratio
Wiring Fabric Horizontal and vertical wire segments of various lengths
Introduction to FPGA video:
https://www.youtube.com/watch?v=EVy4KEj9kZg

## Slide 5: LUT + DFF Lattice Semiconductor iCE40FamilyHandbook.pdf pg6-2

## Slide 6: Input – Output pins Lattice Semiconductor iCE40FamilyHandbook.pdf pg6-7
Notes: Not good to have two connected tri-state drivers fighting each other!

## Slide 7: Block RAM Xilinx Spartan-6 FPGA Block RAM Resources User Guide pg12

## Slide 8: Wiring Fabric Altera CycloneV Device Handbook pg1-2

## Slide 9
The chip manufacturers
Xilinx (now AMD): www.xilinx.com
  Originated FPGAs with help from AMD
Altera (now Intel): www.altera.com
  Originally CPLDs, #2 in FPGAs.
Microsemi (was originally Actel): www.microsemi.com/product-directory/1636-fpga-soc
  SRAM & flash based
Lattice Semiconductor: www.latticesemi.com
  Offer tiny FPGA chips
Quicklogic: www.quicklogic.com
  ARM + ~2K LUTs
Gowinsemi: https://www.gowinsemi.com/en/

## Slide 10: FPGA Tools
HDL (Hardware Description Languages)
  VHDL, Verilog, System Verilog
  Also High Level Synthesis(HLS): C, C++, Matlab
  HDL generators: MyHDL(Python), Haskell
Compilation HDL into “gates” & DFF
Place & Route Vendor proprietary
Timing analysis How fast will it run?
Simulation Unit testing on a PC
Download Transfer bit file to the chip

## Slide 11: IP (Intellectual Property) Pre-packaged HDL modules
Opencores.org
  Hundreds of free designs in 16 categories
FPGA vendor IP: Free, Generally fairly simple
  CORDIC: Coordinate Rotation Digital Computer
  Soft processor cores
    Xilinx micro Blaze
    Altera NIOS II
    RISC-V
    For several others see: https://en.wikipedia.org/wiki/Soft_microprocessor
Not Free: Licensing terms vary

## Slide 12: Xilinx CORDIC GUI Ray Andraka 1998: A survey of CORDIC algorithms for FPGA based computers

## Slide 13: Micro Blaze Core Block Diagram Xilinx MicroBlaze Processor Reference Guide pg11

## Slide 14: Key features of Nios II family members Altera Nios II Embedded Processor Backgrounder pg1

## Slide 15: FPGA 201
6LUT/ALM 4:1 mux, 3-input adder
LUT RAM asynchronous read, sync write
Multipliers 9x9 to 27x27 with accumulator
PLL/DLL Phase/Delay Locked Loop
LVDS Low Voltage Differential Signaling
DDR controller Uses ordinary IO pins
  DDR, DDR2, DDR3, DDR4, LPDDR, QDR, RLDDR3
uP cores: Quad ARM Cortex A53, dual R5
SERDES Very high speed serial IO
Notes: ALM is an Altera/Intel term: Adaptive Logic Module roughly equivalent to a 6 Input Lookup Table.

## Slide 16: Simplified DSP48A1 slice Xilinx Spartan-6 FPGA DSP48A1 Slice pg 17
Notes: Right most adder is 48 bits wide. Other vendor adders vary from 56 to 64 bits wide. Multiplier size also varies with vendor and FPGA family.

## Slide 17: Monster FPGA chips
7nm, much product at 16-20nm
4 million LUTs
12K DSP units
480 MB block RAM
Quad-core 64-bit ARM v8 +Mali 400 +H265 codec
6K Floating-point DSP (single precision)
3K LUTs/dollar (announced)
850MHz DSP Fmax
58Gbps SERDES and 64+ channels
Notes: SERDES: interface pins provided with serial to parallel and parallel to serial at very high speeds (billions of bits per second).

## Slide 18: FPGA evaluation kits all use USB download, as of 2015
Vendor Price FPGA “LUTs” Mults Comments
Arrow BeMicro MAX10 $30 Altera Max 10M08 8K 24 oscillator, 12-bit A2D, flash
Schmartboard PSoC5LP $35 Cypress PSoC5 384 0
Has ARM Cortex M3, digital & analog
Arrow BeMicroCV $49 Altera Cyclone V 25K 50
Digilent Cmod S6 $69 Xilinx Spartan-6 4K 4 48-pin DIP
XESS XuLA2-LX9 $69 Xilinx Spartan-6 9K 16 40-pin DIP, SDRAM
Scarab Hardware miniSpartan6+ $75 Xilinx Spartan-6 9K 16 (2) HDMI, 32MB DRAM, microSD
Digilent ZYBO(student $) $125 Xilinx Zynq 7010 28K 80 (2) Cortex A9, 512MB, HDMI…
Adapteva Parallella-16 $149 Xilinx Zynq 7010 28K 80 (2) Cortex A9, 16-core uP
Notes: Prices now about 2X higher. Newer, faster and lower power chips now available.

## Slide 19: Neat Projects
Cray-1: Runs as fast as original, on $100 FPGA board
Mandelbrot set: PS2 display, 30 frames/sec
MiSTer: Video gaming with exact timing
Retro computers
  PDP8
  PDP11
  PDP11/70
Notes: Many open source versions of 8-bt microprocessors (6502, Z80 etc.)

## Slide 20: Cray-1 http://www.chrisfenton.com/homebrew-cray-1a/
Notes: Spartan-3E FPGA board in the base of the CRAY-1 model (on left), actual CRAY-1 center.

## Slide 21: MiSTer gaming engine
Notes: https://retrogamecoders.com/mister-fpga-tutorial-getting-started-with-mister/

## Slide 22: PDP11 retro computer http://pdp2011.sytse.net/wordpress/
Notes: DEC PDP11/70 chassis behind terminal, FPGA card above keyboard

## Slide 23: FPGA Literature
Harris & Harris 2013: the very best textbook
  Digital Design and Computer Architecture, 2nd ed.
Maxfield 2004: folksy, good at silicon
  The Design Warrior’s Guide to FPGAs
Peter Chambers: free web PDF
  The Ten Commandments of Excellent Design
Mealy & Tappero 2012: no-frills VHDL, free web PDF
  Free Range VHDL

## Slide 24: Videos & Training
Xilinx
http://www.xilinx.com/training/free-video-courses.htm
http://www.xilinx.com/support/university.html
Videos available via vivado help menu
Altera
https://www.altera.com/support/training/university/overview.html

## Slide 25: Ten Commandments for Successful Design
1. All state machine outputs shall always be registered
2. Thou shalt use registers, never latches
3. Thy state machine inputs, including resets, shall be synchronous
4. Beware fast paths lest they bite thine ankles
5. Minimize skew of thine clocks
6. Cross clock domains with the greatest of caution. Synchronize thy
signals!
7. Have no dead states in thy state machines
8. Have no logic with unbroken asynchronous feedback lest the fleas of
myriad Test Engineers infest thee
9. All decode logic must be crafted carefully—eschew asynchronicity
10. Trust not thy simulator—it may beguile thee when thy design is junk

## Slide 26: David Harris & Sarah Harris 2013 Digital Design & Computer Architecture
From FET transistors to x86
VHDL and System Verilog side by side
Implements MIPS core three ways
  Single clock
  Multi-clock, e.g. state machine
  Pipelined
Each chapter has interview questions
Book versions for ARM and RISC-V

## Slide 27: Free Range VHDL

## Slide 28: Guidelines
“Fundamental mode”: Single clock, no latches
Two process VHDL:
  Distinct combinational and sequential processes
  Jiri Gaisler 2014: A structured VHDL design method
Metastability: when a signal crosses clock domains, setup & hold violations occur
VHDL, Verilog and System Verilog Quick Reference Cards

## Slide 29: Insights
You are master of both time and space
Think like the compiler to write good code
Pack a FPGA over 80% full & timing suffers
Takes more effort than writing software
  Large projects are team projects
  Specialization occurs
FPGA knowhow is a necessary skill
Hands-on seminars often have evaluation kit bargains

## Slide 30: Vendor History
Xilinx (purchased by AMD)
  Founded 1984 (38 years ago)
  Invented the FPGA (Ross Freeman)
  Has tried a number of FPGA architectures
  Purchased AutoESL Design in 2011
    Converts C, C++ or SystemC into VHDL or Verilog
  Replaced ISE tool with Vivado in 2012
  PYNQ: Python for FPGA boards with ARM uP

## Slide 31: Vendor History
Altera (purchased by Intel)
  Founded 1983
  PLD (Programmable Logic Device) market leader
  Has migrated to a FPGA product line
  Purchased Enpirion in 2013
    Maker of DC2DC converters
  Using Intel as a foundry for 22nm & 14nm parts

## Slide 32: Vendor History
Lattice Semiconductor
  Founded 1983
  Originally made RAM
  Major CPLD vendor
  Bought Vantis (AMD spinoff) in 2000
  Bought Agere FPGA group (Lucent spinoff) in 2002
  Bought Silicon Blue (40nm low power startup)
  Bought Silicon Image in 2015

## Slide 33: Vendor History
Actel (now Microchip)
  Founded 1985
  Acquired by Microsemi Corp. in 2010
  Anti-fuse FPGAs for military & space
    Radiation tolerant
    High reliability
    Live on power-up
  Mixed signal products in 2005
  Have moved into the high security market

## Slide 34: Books
Harris & Harris 2013: Digital Design and Computer Architecture, 2nd ed.
VHDL & System Verilog, all the way from 0s & 1s to x86
Max Maxfield 2004: The Design Warrior’s Guide to FPGAs
Folksy, good coverage at the chip level
Nazeih Botros 2006: HDL Programming Fundamentals – VHDL and Verilog
Side by side VHDL & Verilog
Peter Ashenden 2008: The Designer’s Guide to VHDL, 3rd ed.
The VHDL reference
Steve Kilts 2007: Advanced FPGA Design

## Slide 35: Free PDFs
Mealy & Tappero 2012:
  Free Range VHDL: A to-the-point VHDL text
Crockett etal 2014:
  The Zynq Book: ARM Cortex A9 + FPGA
Jiri Gaisler 2014:
  A structured VHDL design method
Ray Andraka 1998:
  A survey of CORDIC algorithms for FPGA based computers
Notes: Github/jimbrake/FPGA_Boot_Camp has spreadsheet with 20+ book length PDFs

## Slide 36: EDA (Electronic Design Automation)Tools
Xilinx ISE (depreciated), Vivado
Altera Quartus
Actel Libero
Lattice Diamond
Cypress PSoC Creator
MathWorks MATLAB, Simulink
Synopsys Design Compiler, Synplicity
Mentor Exemplar, Precision, Model Sim
Aldec Active HDL
Altium PCB design, was supporting FPGAs

## Slide 37: Hello World for FPGAs Avnet s6microboard