## Slide 1: First Day Slides Boot Camp for Digital Systems Education Circuit Simulation & RTL generation
Jim Brakefield jim.brakefield@ieee.org
IEEE Computer Society
Notes: Tinker toy construction embodies the generation/design of objects from simple uniform components

## Slide 2: Preliminaries
Classroom provided by St. Mary’s University
Funding provided by a grant from the IEEE Computer Society as part of their Emerging Technologies program
I’m Jim Brakefield, jim.brakefield@ieee.org
Today’s web site: https://events.vtools.ieee.org/m/321262
Slides only, Flash drives have full set of files (20MB)
  Also at https://github.com/jimbrake/FPGA_Boot_Camp
Introduction to FPGA video: https://www.youtube.com/watch?v=EVy4KEj9kZg
Lunch today at St. Mary’s cafeteria (line up at counter and the IEEE grant will pick up the tab)

## Slide 3: Today’s Agenda
View Youtube video
Review of digital logic & binary
Download Digital simulator
  Or copy from flash drive
Exercise simulator (many example schematics)
Add Boolean Board configuration files
Install configuration files
Create new schematic with IO pins
Save VHDL or Verilog RTL of schematic
Inspect RTL

## Slide 4: Not quite free
Using the grant money to buy an FPGA board for each student (and lunch), the idea being that way each student can spend more time on the board.
In return for the “free” FPGA board, you e-mail a progress report periodically to jim.brakefield@ieee.org
Part of the grant is to determine the viability of this approach to FPGA education, hence need feedback.

## Slide 5
My view of binary
Zero and ones: One names a single such signal or a group of such signals (subscripted by bit number)
A binary number is a polynomial:
  A[n-1]xn-1 + A[n-2]xn-2 + … A[1]x1 + A[0]x0
  Where X = 2, and A[n] are 0 or 1 bits from the number. If A[n-1] is 0/-1 then it is 2’s complement and negative if A[n-1] is -1.
  It is typical for the bit numbers to run from N-1 to 0 where N is the number of bits.
  Adding or subtracting 2’s complement wraps around in a circle where the most positive and most negative numbers are adjacent (any carry or borrow beyond xn-1 is discarded).
8/26/2022
5
Notes: For me this approach has the cleanest understanding of signed 2’s complement arithmetic.

## Slide 6: Interactive digital simulation
Schematic editor and simulator
Provides an intermediate step before RTL (Register Transfer Logic) and full FPGA tools.
Requires nothing beyond a PC.
Requires Java
Totally interactive
Generates VHDL or Verilog RTL files
Generates constraint file for vivado (xilinx FPGA tool)
Notes: The two main RTLs are verilog and VHDL. Most recent verilog is called System Verilog. ASIC people prefer verilog. DOD and Europe like VHDL. There are linting tools that can check your code.

## Slide 7: “Digital” logic simulator
Web site: https://github.com/hneemann/Digital/
Authored by: Helmut.Neemann@mosbach.dhbw.de
Open source, other simulators available
Modified to support the Boolean board
  BASYS3.config renamed to Boolbd.config
  BASYS3_IO.dig renamed to Boolbd.dig
  And pin assignments updated
  And PMOD pins moved to Boolbd_pmod.dig
  In the subdirectory examples/hdl
  Boolbd.* files are read only

## Slide 8: Digital web page https://github.com/hneemann/Digital/
Is 12MB zip file
22MB unzipped
Must have Java installed
Notes: Is 12MB zip file 22MB unzipped. Approximately monthly updates to the software.

## Slide 9: Unzipped Digital directory Double click on either *.exe

## Slide 10: Initial Digital screen will change to last schematic you viewed
Note: Clock references, bus width indicators.
Small triangles are named signal references, e.g. implied connections.
Tri-states not used within FPGAs.
Right click on an icon to see/set data width.
Notes: This in the file Digital/examples/processor/Processor.dig. Digital remembers the last schematic somewhere on your PC.
Note: Clock references, bus width indicators, tri-states not used in FPGAs. Right click on an icon to see/set data width.
From examples/processor/Processor.dig. https://github.com/hneemann/Assembler has the processor assembler.

## Slide 11: High res github.com/hneemann/Digital
Notes: Note: Clock references, bus width indicators. Tri-states not used within FPGAs. Right click on an icon to see/set data width.
From examples/processor/Processor.dig. https://github.com/hneemann/Assembler has the assembler.

## Slide 12: Configure Digital for Boolean Board
Copy
To:
Notes: Boolbd.config and Boolbd_Ios.dig are in the _boolbd_config directory

## Slide 13: Configure for Boolean Board
Go to Edit Settings Advanced
Specify Toolchain Configuration file
From examples/hdl select Booleanbd.config
Notes: To un-configure erase the “Toolchain Configuration” entry. *.config file has the new menu item name (Boolbd) on line 2(in case of a rename)

## Slide 14: Digital with additional menu item always starts with last schematic, here the Boolean board IO pins
Notes: After opening Boolbd_Ios.dig This is write protected, save to new file to edit. A starting point for you FPGA board design: prune and add circuits!

## Slide 15: Drawing a rectangle for cut & paste or delete point & drag with mouse

## Slide 16: Insert into “new” and “save as”

## Slide 17: Connect switches to LEDs
Point at a red dot,
release,
move to LED dot
and release
Add logic gates
from Components
Add clock from IO
Add D flip-flop
  from Flip-Flops
Notes: There is a choice of using Digital icons for simulation only or using Boolean board icons for both simulation and RTL generation.

## Slide 18: Inspecting switch or LED
Right click
Basic menu
Number of data bits &
Label for switch

## Slide 19: Inspecting switch or LED
Advanced menu
Rotation
Pin number
  Is FPGA chip pin #
  Can be found on
  Boolean Board schematic
  Or in the Boolean Board constraint file

## Slide 20: Boolean Board Resources https://www.realdigital.org/hardware/boolean
Schematic is PDF file of board
XDC for downloading constraint text file
Getting started goes to reference manual web page

## Slide 21: Basic Digital tutorials https://www.realdigital.org/course/digital-logic-for-the-boolean-board
Notes: Web page recently updated

## Slide 22: Wikipedia basic logic circuits
Full adder https://en.wikipedia.org/wiki/Adder_(electronics)
Multiplexer https://en.wikipedia.org/wiki/Multiplexer
ALU https://en.wikipedia.org/wiki/Arithmetic_logic_unit
  Has easy to understand VHDL source code
Barrel shifter https://en.wikipedia.org/wiki/Barrel_shifter
Wallace tree multiplier https://en.wikipedia.org/wiki/Wallace_tree
Synchronous binary up counter
  In schematic form: change a Dff if all preceding Dff are all 1
  In RTL: “if enable AND rising-clock then count <= count+1”
Notes: Didn’t find good examples of up counter?

## Slide 23: What do FPGA tools do?
Much goes on behind the scenes
Circuit is optimized (logic simplification)
  unused stuff is pruned, if no outputs then all pruned
Circuit is mapped into FPGA primitives
Circuit wired up with FPGA routing resources
Bit file generated that configures the chip
Error checking especially missing semicolons
Reports on timing, resources used, error messages
Schematic viewer will show chip details
Notes: Schematic viewer shows FPGA chip floor plan, the actual layout of LUTs, DFF, DSP units and Block RAMs.

## Slide 24: Boolean board $69/$79
Notes: Uses AMD/xilinx tools(vivado). The staggered IO holes is deliberate, will hold and connect headers without soldering. HDMI video out. Available with or without Bluetooth LE.

## Slide 25: Boolean Board background
RealDigital.org
  Educational mission
  Very well done courseware, uses hyper links
  Have added additional boards to their web site
Board uses AMD/xilinx Spartan-7 FPGA
  Full part number: XC7S50-CSGA324
  50K logic cells (33K 6-LUTs)
  2.8M bits of block RAM (300K bytes)
  One of the least expensive FPGA boards with full user IO, also servo headers & potentiometer
Notes: If time & budget allows will do the course with the DE10-Lite board (in the fall).

## Slide 26: RealDigital.org
Notes: For more advanced work, especially using ARM cores PYNQ-Z2 a better choice over Blackboard: Has Xilinx PYNQ tool set. Serial port used for IO when ARM core present. The three boards on bottom added in last two months. Show a dedication to advanced capabilities.

## Slide 27: Downloading vivado now has an ITAR notice
https://www.xilinx.com/support/download.html
https://www.xilinx.com/support/installer/installer-info-general.html
Use the web installer (212MB) and only install for Spartan-7 devices. Full install is a 74GB tar.gz file!!
Will still take time (~2hrs) and 44GB download!
Takes 71GB of disk space!! 
Follow RealDigital Boolean Board instructions at https://www.realdigital.org/doc/1fd3322461ac4bcc1fcd6bcc6c5907ec
Can add additional FPGA devices later
Hundreds of video tutorials (use help button)
Notes: Took 3 hours total at 100Mb/sec download speed. I did not turn off anti-virus protection.

## Slide 28: Educational programs
Intel/Altera academy Quartus: RTL & Schematic
AMD/Xilinx university program ISE & Vivado RTL tools
Courseware for Real Digital Boolean board RTL
  https://www.realdigital.org/course/digital-logic-for-the-boolean-board
https://www.tina.com/ (Schematic based, not free)
  Support for the Digilent Basys 3 and the Terasic DE10-Lite FPGA boards
  https://www.tina.com/blog/programming-fpga-boards-with-tina-using-schematic-design-entry/
Digital logic simulator (Schematic based)
    Support for the Digilent Basys 3 and the TinyFPGA-BX boards
  https://github.com/hneemann/Digital/
Notes: RTL: Register transfer language, usually VHDL or Verilog. Quartus and Vivado are mainstream tools with free education variants (have reduced FPGA family support). Xilinx ISE not recommended for new users.

## Slide 29: Intel/Altera academic program
https://www.intel.com/content/www/us/en/developer/topic-technology/fpga-academic/overview.html
https://www.intel.com/content/www/us/en/developer/topic-technology/fpga-academic/materials.html
https://fpgacademy.org/tools.html
DE10-Lite academic price $77
Notes: Only two push buttons. Least expensive Altera board with “full” user IO. Altera tools support schematic capture.

## Slide 30: Xilinx university program
https://www.xilinx.com/support/university.html
https://www.xilinx.com/support/university/xup-boards.html
$69 $123 $200
$549
$2149
Notes: Boolean Board “endorsement” by Xilinx. Kria-KV260 has state-of-the-art FPGA, heavily backordered.

## Slide 31: FPGA Application Areas
Communications
DSP
Software-defined radio
Aerospace and defense systems
ASIC prototyping
Medical imaging
Computer vision
Speech recognition
Cryptography
Bioinformatics
Computer hardware emulation
Data Center: AI, NN, big data
Advantages:
Outstanding Job market
Disadvantages:
Tough learning curve

## Slide 32: The chip manufacturers
Xilinx (now AMD): www.xilinx.com
  Originated FPGAs with help from AMD
Altera (now Intel): www.altera.com
  Originally CPLDs, #2 in FPGAs.
Microsemi (was originally Actel): www.microsemi.com/product-directory/1636-fpga-soc
  SRAM & flash based
Lattice Semiconductor: www.latticesemi.com
  Offer tiny FPGA chips
Quicklogic: www.quicklogic.com
  ARM + ~2K LUTs
Gowinsemi: https://www.gowinsemi.com/en/

## Slide 33: FPGA References
Twelve youtube videos on specific FPGA features (uses verilog RTL): https://www.youtube.com/playlist?list=PLEBQazB0HUyT1WmMONxRZn9NmQ_9CIKhb
Three Ages of FPGAs: A Retrospective…, Steve Trimberger, Proc. IEEE v103#3p318, 2015
  www.cpe.virginia.edu/grads/pdfs/January%202016/VLSI.pdf
  https://www.youtube.com/watch?v=4ntXSyOhlBY
  Xilinx Part Family History, John Lazzaro,
  www-inst.eecs.berkeley.edu/~cs294-59/fa10/resources/Xilinx-history/Xilinx-history.html
Altera History, corporate, http://www.fundinguniverse.com/company-histories/altera-corporation-history/
  www.altera.com/about/company/history.html
Low cost FPGA boards
  https://www.joelw.id.au/FPGA/CheapFPGADevelopmentBoards
Open source IP https://opencores.org/projects
Notes: Many open source projects using FPGAs on Github.

## Slide 34: Built-in IO Done Just Right
10+ slide switches or DIP switches
6+ push buttons
10+ LEDs, two tri-color (RGB)
7-segment LEDs (four to eight digits)
VGA or HDMI connector
Expansion IOs
  Arduino, Pi, PMOD, Grove, DIP pattern…

## Slide 35
Nice to have built-in IO
Potentiometer or incremental encoder
Servo connector(s)
Navigation switch or rhombic push button pattern
Pmod connector(s)
Grove connector(s)
Built-in microprocessor (usually ARM)
SRAM or DRAM (for microprocessor support)
SD socket (for microprocessor OS)
Notes: The servo connectors make for a robotics capable board. Usage model for potentiometer is showing the voltage on the 7-segment display. Those ready to do soft core or built in processor probably don’t need switches, LEDs and 7-segment displays; use serial terminal instead.

## Slide 36: Under $40 & some built-in IO
Seeedstudio Spartan-7 Edge
Accelerator board $40
Seeedstudio
Gowin RUNBER $30
StepFPGA MAX10 dev board $39
Notes: Four digit 7-segment display with 5 push buttons Arduino shield for Edge Accelerator $9 (uses I2C).

## Slide 37: Very little built-in IO $25-30
iCE40
Feather
Has battery
support
UPDuino v3.1
Trenz MAX-1000
Has 8MB ram

## Slide 38: Very little built-in IO $15
Notes: Uses Gowin GW1NR-9 FPGA: ARM Cortex M3, 8K LUTs, 2 push buttons, 6 LEDs, HDMI connector, SD slot, DRAM, LCD connector

## Slide 39
FPGA board rankings
Top version sorted by LUT count, bottom version by block RAM bit count
This listing is only a sample of the hundreds of boards available.
8/26/2022
39

## Slide 40: In conclusion
It is thought that ownership of an FPGA board will lead to greater usage and knowledge. As opposed to shared laboratory equipment.
Oriented towards a beginner’s board at low cost. Lots of switches, LEDs etc. eliminate need for discrete components and their fragile wiring.
These slides, future class dates and registration links at: https://events.vtools.ieee.org/m/318519
Next class (September 3) registration link: https://events.vtools.ieee.org/m/321263
  Registration not required for Sept. 3rd class.