## Slide 1: Second Day Slides Boot Camp for Digital Systems Education Running generated RTL thru Vivado
Jim Brakefield jim.brakefield@ieee.org
IEEE Computer Society
Notes: Tinker toy construction embodies the generation/design of objects from simple uniform components

## Slide 2: Preliminaries
Classroom provided by St. Mary’s University
Funding provided by a grant from the IEEE Computer Society as part of their Emerging Technologies program
I’m Jim Brakefield, jim.brakefield@ieee.org
https://events.vtools.ieee.org/m/318519
Slides only, Flash drives have full set of files (20MB)
  Also at https://github.com/jimbrake/FPGA_Boot_Camp
Introduction to FPGA video: https://www.youtube.com/watch?v=EVy4KEj9kZg

## Slide 3: mess of wires not cool any more
From https://life.ieee.org/
In today’s world
most wires are
in the PCB and
In the FPGA !
OK as long as you
don’t need to
move the device
Need a photo of
your work as a
replacement

## Slide 4
My view of binary
Zero and ones: One names a single such signal or a group of such signals (subscripted by bit number)
A binary number is a polynomial:
  A[n-1]xn-1 + A[n-2]xn-2 + … A[1]x1 + A[0]x0
  Where X = 2, and A[n] are 0 or 1 bits from the number. If A[n-1] is 0/-1 then it is 2’s complement and negative if A[n-1] is -1.
  It is typical for the bit numbers to run from N-1 to 0 where N is the number of bits.
  Adding or subtracting 2’s complement wraps around in a circle where the most positive and most negative numbers are adjacent (any carry or borrow beyond xn-1 is discarded).
7/20/2022
4

## Slide 5: Today’s agenda
Update Digital with Pmod IOs
What’s on the FPGA board
FPGA parts (LUTs, Block RAM, DSP, IO, fabric)
Review of digital logic & binary
Summary of VHDL/Verilog
Summary of constraint files
Do a Vivado project

## Slide 6: Today’s agenda
Who hasn’t got Vivado installed?
  Have a disk drive & flash drive with install files
  Will take 30+minutes
Who hasn’t generated VHDL or Verilog from their schematic?
A picture of everyone with their FPGA board

## Slide 7: Boolean Board IOs Boolbd_IOs.dig
https://github.com/jimbrake/FPGA_Boot_Camp

## Slide 8: Boolean Board Pmod IOs Boolbd_Pmods_PCB_view.dig
https://github.com/jimbrake/FPGA_Boot_Camp

## Slide 9: Boolean Board Pmod IOs Boolbd_Pmods_schematic_view.dig
https://github.com/jimbrake/FPGA_Boot_Camp

## Slide 10: RTL (Register Transfer Language)
Separates design into combinatorial (logic) and sequential (registers).
For simple designs use a single clock
  Boolean Board clock input is 100MHz
  Digital will generate slower clocks
    Right click on clock icon & set frequency
Registers update on rising edge clock

## Slide 11: Schematic for project
fresh_start.dig schematic

## Slide 12: fresh_start VHDL part 1

## Slide 13: fresh_start VHDL part 2

## Slide 14: fresh_start VHDL part 3

## Slide 15: Side by side VHDL and Verilog
Digital generates both
RealDigital’s treatment:
  https://www.realdigital.org/downloads/e06bddc63669cbc91ae981df18bcf3c5.pdf
Side by side System-Verilog & VHDL:
  Digital Design and Computer Architecture, Harris & Harris, 2nd ed. Also ARM and RISC-V editions
  Highly recommended, goes from transistors to PCs
Also: https://www.fpga4student.com/2017/08/verilog-vs-vhdl-explain-by-example.html

## Slide 16: Side by side VHDL and Verilog cont’d
Clive “Max” Maxfield’s books:
  The Design Warrior's Guide to FPGAs, 2004
  FPGAs: World Class Designs, 2009
  Electrical Engineering: Know It All, 2011
    covers the entire field, chapters are written by others

## Slide 17: Basic Digital tutorials https://www.realdigital.org/hardware/boolean

## Slide 18: What do FPGA tools do?
Much goes on behind the scenes
Circuit is optimized (logic simplification)
  unused stuff is pruned, if no outputs then all pruned
Circuit is mapped into FPGA primitives
Circuit wired up with FPGA routing resources
Bit file generated that configures the chip
Error checking especially missing semicolons
Reports on timing, resources used, error messages
A schematic viewer will show chip details

## Slide 19: LUTs
Performing Boolean Algebra inside an FPGA using Look-Up Tables (LUTs)
https://nandland.com/lesson-4-what-is-a-look-up-table-lut/:
Note to the reader: many textbooks and classrooms will spend a
significant amount of time discussing how LUTs can be wired to
create the optimal solution to a Boolean expression. Optimal
means that it uses the least number of gates possible. Topics
such as De Morgan’s Law, Karnaugh Maps, the Quine-McCluskey
method, and others are usually discussed at great length that
describe how to optimize digital logic. However I feel that this is
not necessary to begin learning about FPGAs.

## Slide 20: Block RAM tutorial
https://nandland.com/lesson-15-what-is-a-block-ram-bram/

## Slide 21: Boolean board $69/$79
Notes: Uses AMD/xilinx tools(vivado). The staggered IO holes is deliberate, will hold and connect headers without soldering. HDMI video out. Available with or without Bluetooth LE.
Digital schematic tool: Three *.dig files: base IO, Pmod schematic view, Pmod PCB vies (

## Slide 22: Boolean Board background
RealDigital.org
  Educational mission
  Very well done courseware, uses hyper links
  Have added additional boards to their web site
    Some that are very advanced!
Board uses AMD/xilinx Spartan-7 FPGA
  50K logic cells (33K 6-LUTs)
  2.8M bits of block RAM (300K bytes)
  One of the least expensive FPGA boards with full user IO, also servo headers & potentiometer
Notes: If time & budget allows will do the course with the DE10-Lite board (in the fall).

## Slide 23: Downloading vivado
https://www.xilinx.com/support/download.html
https://www.xilinx.com/support/installer/installer-info-general.html
Use the web installer (212MB) and only install for Spartan-7 devices. Full install is a 74GB tar.gz file!!
Will still take time: 44GB download!
Takes 71GB of disk space!! 
Follow RealDigital Boolean Board instructions at https://www.realdigital.org/doc/1fd3322461ac4bcc1fcd6bcc6c5907ec
Can add additional FPGA devices later
Hundreds of video tutorials (use help button)
Notes: Took 3 hours total at 100Mb/sec download speed. Did not turn off anti-virus protection.

## Slide 24: Creating a Vivado project
Double click Vivado 2022.1 icon
File/Project/New/Next

## Slide 25: Creating a Vivado project step 2
Project Type: RTL
Add Sources: Next

## Slide 26: Creating a Vivado project step 3
Add Sources: Add Files

## Slide 27: Creating a Vivado project step 4
Pick VHDL or Verilog files from your directory
Next (will copy & add files to project)

## Slide 28: Creating a Vivado project step 5
Add constraint file

## Slide 29: Creating a Vivado project step 6
Need to get this exactly right

## Slide 30: Creating a Vivado project step 7
Finish

## Slide 31: Creating a Vivado project step 8
Generate Bitstream will do the following:
RTL ANALYSIS
SYNTHESIS
IMPLEMENTATION
PROGRAM AND DEBUG
And report any errors
Digital generated RTL should not have errors!

## Slide 32: Creating a Vivado project step 9
After several minutes and no errors
Check Utilization, I prefer “Table”
  LUT count, DFF count, etc.
  IO should match your design
  BUFG is for the clock input
Post Synthesis is an initial estimate
Post Implementation is final usage
For a simple design Power is < 0.1 Watt

## Slide 33: Creating a Vivado project step 10
Open Hardware Manager (board plugged in and turned on)

## Slide 34: Creating a Vivado project step 11
Open Target – Auto Connect – Program device
Turn switch 3 on
  LED 4 will blink every two seconds
  Other switches control other LEDs
Success!

## Slide 35: Archive Project
File/Project/Archive
Creates zip file of 779KB, full project is 3.5MB
Programming file: Main.bit (2,141KB) is compressed!

## Slide 36: Vivado project summary

## Slide 37: FPGA References
Three Ages of FPGAs: A Retrospective…, Steve Trimberger, Proc. IEEE v103#3p318, 2015
  www.cpe.virginia.edu/grads/pdfs/January%202016/VLSI.pdf
  https://www.youtube.com/watch?v=4ntXSyOhlBY
  Xilinx Part Family History, John Lazzaro,
  www-inst.eecs.berkeley.edu/~cs294-59/fa10/resources/Xilinx-history/Xilinx-history.html
Altera History, corporate, http://www.fundinguniverse.com/company-histories/altera-corporation-history/
  www.altera.com/about/company/history.html
Low cost FPGA boards
  https://www.joelw.id.au/FPGA/CheapFPGADevelopmentBoards
Open source IP https://opencores.org/projects
Github projects: search on “github vhdl verilog cpu”

## Slide 38: Not quite free
Using the grant money to buy an FPGA board for each student (and lunch), the idea being that way each student can spend more time on the board.
In return for the “free” FPGA board, you e-mail a progress report periodically to jim.brakefield@ieee.org
Part of the grant is to determine the viability of this approach to FPGA/Digital System education, hence need feedback.

## Slide 39: In conclusion
It is thought that ownership of an FPGA board will lead to greater usage and knowledge. As opposed to shared laboratory equipment.
Oriented towards a beginner’s board at low cost. Lots of switches, LEDs etc. eliminate need for discrete components and their fragile wiring.
Future class dates and registration links at: https://events.vtools.ieee.org/m/316279

## Slide 40: PYNQ-Z2 $123 at Newark (for the more advanced user)
FPGA boards with microprocessor cores typically use serial terminal
for user IO and thus fewer switches, buttons & LEDs needed
Notes: FPGA board with two ARM A9 cores. Available at RealDigital and Newark. See http://www.pynq.io for it’s software infrastructure!

## Slide 41: FPGA board rankings
Top version sorted by LUT count, bottom version by block RAM bit count
This listing is only a sample of the hundreds of boards available.
Notes: The spreadsheet at https://events.vtools.ieee.org/m/306653 has a sheet with a long somewhat dated list sorted by FPGA family. Also a sheet sorted by shape. ATD: analog to digital converter. LUT: logic lookup table. Block RAM: typically dual ported, adjustable aspect ratio.

## Slide 42: MiniStar experiment kit $69 Gowin FPGA with ARM Cortex M3
Notes: A low cost board/FPGA with Cortex M3. Available at Amazon for $69. 4K LUTs, 8MB SRAM. Kit has connection cables. 4 slide & 4 DIP switches, 6 PB, 12 LED, 2 Grove connectors, and the four digit 7-segment display.

## Slide 43: Educational programs
Intel/Altera academy Quartus: RTL & Schematic
AMD/Xilinx university program ISE & Vivado RTL tools
Courseware for Real Digital Boolean board RTL
  https://www.realdigital.org/course/digital-logic-for-the-boolean-board
https://www.tina.com/ (Schematic based, not free)
  Support for the Digilent Basys 3 and the Terasic DE10-Lite FPGA boards
  https://www.tina.com/blog/programming-fpga-boards-with-tina-using-schematic-design-entry/
Digital logic simulator (Schematic based)
    Support for the Digilent Basys 3 and the TinyFPGA-BX boards
  https://github.com/hneemann/Digital/
Notes: RTL: Register transfer language, usually VHDL or Verilog. Quartus and Vivado are mainstream tools with free education variants (reduced FPGA family support). Xilinx ISE not recommended for new users.

## Slide 44: Intel/Altera academic program
https://www.intel.com/content/www/us/en/developer/topic-technology/fpga-academic/overview.html
https://www.intel.com/content/www/us/en/developer/topic-technology/fpga-academic/materials.html
https://fpgacademy.org/tools.html
DE10-Lite academic price $77
Notes: Only two push buttons. Least expensive Altera board with “full” user IO. DRAM and micro SD slot facilitate use of Altera/Intel NIOS-II soft core processor.

## Slide 45: Xilinx university program
https://www.xilinx.com/support/university.html
https://www.xilinx.com/support/university/boards-portfolio/xup-boards/RealDigitalBoolenBoard.html
$69 $123 $200
Notes: Boolean Board “endorsement” by Xilinx. Kria-KV260 has state-of-the-art FPGA, heavily backordered.